Bonding Snippet Usage

This documentation describes a method to create bonded network interfaces during provisioning. It has not been thoroughly tested due to equipment limitations, but the resultant configuration files should be correct.
# Create the Provisioning Template for Bonding
From the Foreman user interface, select More and then Provisioning from the drop down menu. Select Provisioning Templates from the newly presented drop down menu.
Select New Template and a New Template screen appears. Enter bond_interfaces in the Name field and select the Snippet field to place a checkmark in it.
Place the following code in the Template editor window.
Snippet: bond_interfaces
declare -A bonds=<%= @host.params["bonds"] %>
declare -A bond_opts=<%= @host.params["bond_opts"] %>
declare -A bond_ifaces=<%= @host.params["bond_ifaces"] %>
for bond in ${!bonds[@]}
do
 read parms <<< $( tr -d '\r' <<< ${bonds[$bond]} )
 unset bond_info
 declare -A bond_info=( \
        [DEVICE]="${bond}" \
        [PROTO]="dhcp" \
        [ONBOOT]="no" \
        [NM_CONTROLLED]="no" \
        )
 for parm in ${parms}
 do
   case $parm in
        onboot ) bond_info[ONBOOT]="yes"
        ;;
        none ) bond_info[PROTO]="none"
        ;;
        static ) bond_info[PROTO]="static"
        ;;
        dhcp ) bond_info[PROTO]="dhcp"
        ;;
        vlan ) bond_info[VLAN]="yes"
        ;;
*.*.*.*/*.*.*.* ) read IP NETMASK <<< $( tr '/' ' ' <<< ${parm} )
        bond_info[IP]="${IP}"
        bond_info[NETMASK]="${NETMASK}"
        ;;
   esac
 done
 cat << EOB > /etc/sysconfig/network-scripts/ifcfg-${bond}
DEVICE=${bond}
ONBOOT=${bond_info[ONBOOT]}
NM_CONTROLLED=${bond_info[NM_CONTROLLED]}
BOOTPROTO=${bond_info[PROTO]}
BONDING_OPTS="$( tr -d '\r' <<< ${bond_opts[$bond]} )"
EOB
 [[ "${bond_info[PROTO]}" = "static" ]] && cat << EOB >> /etc/sysconfig/network-scripts/ifcfg-${bond}
IPADDR=${bond_info[IP]}
NETMASK=${bond_info[NETMASK]}
EOB
 [[ "${bond_info[VLAN]}" = "yes" ]] && cat << EOB >> /etc/sysconfig/network-scripts/ifcfg-${bond}
VLAN=${bond_info[VLAN]}
EOB
for iface in $( tr -d '\r' <<< ${bond_ifaces[$bond]} )
do
 cat << EOI > /etc/sysconfig/network-scripts/ifcfg-${iface}
DEVICE=${iface}
BOOTPROTO=none
ONBOOT=${bond_info[ONBOOT]}
MASTER=${bond}
SLAVE=yes
NM_CONTROLLED=no
EOI
 done
done

Select the Submit button at the bottom of the page to save the newly created snippet.
# Update the Kickstart Template
The kickstart template must be modified to use the new snippet. Place the following line inside the %post section of the Kickstart Provisioning Template.
<%= snippets "bond_interfaces" %>

# Configure Host for Bonding
Bonding is configured by setting three Puppet Class Host Parameters, the bonds, bond_ifaces, and bond_opts host parameters. These are added by editing the host in the Foreman interface and selecting the Parameters tab. The + Add Parameter button is used to create new parameters.
## Parameters
The parameters are defined in the format of bash associative arrays. When the parameters are accessed by the snippet, carriage returns are are stripped from the input. This means that carriage returns can be used for readability when setting the Parameter Values. Care should be taken to use carriage returns only between array elements and not withing the array elements themselves.
### bonds
The bonds parameter specifies the basic bond information. It accepts the following options.
onboot	The bond is enabled when the system boots. Default is disabled.
dhcp | static | none	The bond gets its network configuration using DHCP, the network configuration is staticaly configured, or the bond has no network configuration. If none are specified, dhcp is assumed.
vlan	This bond is a VLAN.
x.x.x.x/y.y.y.y	The IP address and Network mask of the interface. Used only when static is specified. Must be in the format presented.

Usage Example:
The following entry defines three bonds: bond0, bond1 and bond1.200. All three bonds are enabled because the onboot option is specified in each definition. bond0 is configured for dhcp. bond1 is configured with no network configuration. bond1.200 is configured as a vlan with static network configuration.
( [bond0]="onboot dhcp" [bond1]="onboot none" [bond1.200]="onboot static vlan 192.168.100.10/255.255.255.0" )
This entry can also be entered into the Foreman interface as:
( [bond0]="onboot dhcp"
[bond1]="onboot none"
[bond1.200]="onboot static vlan 192.168.100.10/255.255.255.0" )
### bond_ifaces
The bond_ifaces parameter specifies the interfaces to use for each bond.

Usage Example:
The following entry assigns eth1, eth4, and eth5 to bond0 and eth0 and eth3 to bond1.
( [bond0]="eth1 eth4 eth5" [bond1]="eth0 eth3" )
### bond_opts
The bond_opts parameter specifies the bonding options to use for each bond. It accepts any valid interface bonding parameters.

Usage Example:
( [bond0]="mode=1 miimon=10" [bond1]="mode=802.3ad" )
# Example Configuration with Bonds and VLANs
The following configuration will configure 5 vlans across two bonds. The first bond uses eth1, eth4, and eth5 for vlans 141, 151, and 170. The second bond uses eth0 and eth3 for VLANs 140 and 150. Both bonds are confgiured for 802.3ad bonding mode. Each VLAN is assigned an IP address on its respective network.
Eth2 is not bonded and is used for provisioning.
## Configuration
Create a parameter with a Name of bonds. Enter the following for its Value.
( [bond0]="onboot none"
[bond1]="onboot none"
[bond0.141]="onboot static vlan 192.168.141.2/255.255.255.0"
[bond0.151]="onboot static vlan 192.168.151.2/255.255.255.0"
[bond0.170]="onboot static vlan 192.168.170.2/255.255.255.0"
[bond1.140]="onboot static vlan 192.168.140.2/255.255.255.0"
[bond1.150]="onboot static vlan 192.168.150.2/255.255.255.0" )

Create a parameter with a Name of bond_ifaces. Enter the following for its Value.
( [bond0]="eth1 eth4 eth5"
[bond1]="eth0 eth3" )

Create a parameter with a Name of bond_opts. Enter the following for its Value.
( [bond0]="mode=803.3ad"
[bond1]="mode=802.3ad" )

## Screenshot

## Resultant Configuration Files
ifcfg-bond0
DEVICE=bond0
ONBOOT=yes
NM_CONTROLLED=no
BOOTPROTO=none
BONDING_OPTS="mode=803.3ad"

ifcfg-bond0.141
DEVICE=bond0.141
ONBOOT=yes
NM_CONTROLLED=no
BOOTPROTO=static
BONDING_OPTS=""
IPADDR=192.168.141.2
NETMASK=255.255.255.0
VLAN=yes
ifcfg-bond0.151
DEVICE=bond0.151
ONBOOT=yes
NM_CONTROLLED=no
BOOTPROTO=static
BONDING_OPTS=""
IPADDR=192.168.151.2
NETMASK=255.255.255.0
VLAN=yes

ifcfg-bond0.170
DEVICE=bond0.170
ONBOOT=yes
NM_CONTROLLED=no
BOOTPROTO=static
BONDING_OPTS=""
IPADDR=192.168.170.2
NETMASK=255.255.255.0
VLAN=yes

ifcfg-bond1
DEVICE=bond1
ONBOOT=yes
NM_CONTROLLED=no
BOOTPROTO=none
BONDING_OPTS="mode=802.3ad"

ifcfg-bond1.140
DEVICE=bond1.140
ONBOOT=yes
NM_CONTROLLED=no
BOOTPROTO=static
BONDING_OPTS=""
IPADDR=192.168.140.2
NETMASK=255.255.255.0
VLAN=yes

ifcfg-bond1.150
DEVICE=bond1.150
ONBOOT=yes
NM_CONTROLLED=no
BOOTPROTO=static
BONDING_OPTS=""
IPADDR=192.168.150.2
NETMASK=255.255.255.0
VLAN=yes

ifcfg-eth0
DEVICE=eth0
BOOTPROTO=none
ONBOOT=yes
MASTER=bond1
SLAVE=yes
NM_CONTROLLED=no

ifcfg-eth1
DEVICE=eth1
BOOTPROTO=none
ONBOOT=yes
MASTER=bond0
SLAVE=yes
NM_CONTROLLED=no

ifcfg-eth2 - Original Configuration, configured by Foreman standard provisioning.
DEVICE="eth2"
BOOTPROTO="dhcp"
DHCP_HOSTNAME="testhost.example.org"
HOSTNAME="testhost.example.org"
HWADDR="02:00:00:00:60:F0"
IPV6INIT="yes"
MTU="1500"
NM_CONTROLLED="yes"
ONBOOT="yes"
TYPE="Ethernet"
UUID="f7527188-d3a3-4e6a-bff0-c9cc010f8a43"

ifcfg-eth3
DEVICE=eth3
BOOTPROTO=none
ONBOOT=yes
MASTER=bond1
SLAVE=yes
NM_CONTROLLED=no

ifcfg-eth4
DEVICE=eth4
BOOTPROTO=none
ONBOOT=yes
MASTER=bond0
SLAVE=yes
NM_CONTROLLED=no

ifcfg-eth5
DEVICE=eth5
BOOTPROTO=none
ONBOOT=yes
MASTER=bond0
SLAVE=yes
NM_CONTROLLED=no