Dell Pilot Deployment Guide

# Configure Foreman Server
If the provisioning interface on the provisioned host is not the first interface returned in the puppet data, Foreman will overwrite the configuration in the database. This can cause issues later.
To prevent Foreman from changing the IP and MAC information to reflect the puppet data, change the ignore_puppet_facts_for_provisioning setting.
- Log into the Foreman user interface.
- Move the mouse over the Administer drop down menu on the right side of the interface.
- Select Settings from the menu.
- Select the Provisioning tab.
- Select Value for the ignore_puppet_facts_for_provisioning setting.
  - Change this setting to true.
## Hammer Command Preparation
During the steps in this document, the hammer command is used to more easily perform the configurations. Usage of the hammer command requires identifiers for the various pieces of information stored within the Foreman server. This includes identifiers for the defined installation media, partitions, templates, hosts, as well as other items.
A checklist file, dell-pilot-checklist.pdf, is available to easily keep track of this information. Download and print the Dell Pilot Checklist from https://wiki.opencrowbar.org/pages/viewpage.action?pageId=6326050.
Write the various information gathered and needed on the checklist for reference as needed.
Several steps in this document use files to configure the environment. These files are available in a TAR file called dell-pilot-deploy.tgz. This TAR fail is available from https://wiki.opencrowbar.org/pages/viewpage.action?pageId=6326050.
Download the tar file and unzip it into the /root/pilot directory..
# mkdir /root/pilot
# cd /root/pilot
# tar xzvf /PATH/TO/FILE/dell-pilot-deploy.tgz

## The hammer command
- Install the packages that contain the hammer command.
  # yum -y install "*hammer*"
  This should install the following packages:
  - rubygem-hammer_cli-doc-0.1.1-12.el6sat.noarch
  - rubygem-hammer_cli-0.1.1-12.el6sat.noarch
  - rubygem-hammer_cli_foreman-0.1.1-16.el6sat.noarch
  - rubygem-hammer_cli_foreman-doc-0.1.1-16.el6sat.noarch
- Configure the hammer command to display 200 items per page. This just makes it easier to read everything.
  - Replace the value for the :per_page: option in the /etc/hammer/cli_config.yml file.
- Configure the hammer command to not prompt for a username/password when connecting.
  - Add the following to the beginning of the /etc/hammer/cli_config.yml file. Replace the name and password appropriately.
    :foreman:
    :username: 'admin'
    :password: 'changeme'
## Hammer help
The hammer command takes the --help option. This option can be used with most of its sub-commands as well. It is useful to see the various options that can be used.
## Configure the Installation Medium
Configure the installation medium that will be used to provision the hosts.
Use the hammer medium create command to add the entry.
The command requires the --name, --os-family and --path options.
The name option should specify a name that is appropriate for the installation.
The os-family should remain Redhat in most cases.
The path option specifies the path or URL to the installation tree.
### Satellite Server
The path included in the example below should work with most satellite installations, just replace SATELLITE_SERVER with the appropriate FQDN.
# hammer medium create --name "Dell OSP Pilot" --os-family Redhat \
 --path 'http://SATELLITE_SERVER/ks/dist/ks-rhel-$arch-server-$major-$version'

### Local ISO on Foreman Node
- mkdir /usr/share/foreman/public/iso
- Copy the RHEL7 iso to the /root directory of the foreman node
- Edit /etc/fstab
- Add the following line to the end:
  /root/RHEL-7.0-Server-x86_64-dvd.iso /usr/share/foreman/public/iso iso9660 loop,ro 0 0
- mount –a
# hammer medium create --name "Dell OSP Pilot" --os-family Redhat \
 --path 'http://FOREMAN_SERVER/iso'

### Local ISO on Solution Admin Host
- On the Solution Admin Host:
  - yum install httpd
  - Configure httpd with any options you want. Defaults will work, but are not secure.
  - copy the ISO to the SAH in /store/data/iso
  - "mount -o loop ISO NAME /mnt"
  - "mkdir /store/data/iso/RHEL6.5" (Name of the OS)
  - "rsync -av /mnt/ /store/data/iso/RHEL6.5"
  - "umount /mnt"
  - "ln -s /store/data/iso/RHEL6.5 RHEL6.5"
- Validate the web interface works
  http://ipaddress of foreman/RHEL6.5/README
## Note the Medium ID
After the medium is created, execute the hammer medium list command.
Take note of the ID (first column) for the newly created medium. This will be needed later.
## Configure the Partition Table
Configure the partition table that the provisioned hosts will use. The partition table is provided in the following file.
dell-pilot.partition	Partition table for the nodes.

Use the hammer partition-table create command to install the partition table. Specify an appropriate NAME for each partition table and specify the file that contains the data.
# hammer partition-table create --name dell-pilot --os-family Redhat \
 --file /root/pilot/dell-pilot.partition

After the partition table is created, execute the hammer partition-table list command.
Take note of the ID of the newly created partition table.
## Configure the Operating System
A definition for the Red Hat Enterprise Linux 7.0 operating system must be created.
Create a new operating system definition for Red Hat Enterprise Linux 7.0.
Use the hammer os create command to create the definition.
# hammer os create --name "RedHat" --major 7 --minor 0 --family Redhat

After creating the operating system, execute the hammer os list command.
Take note of the ID for the new RedHat 7.0 operating system.

Associate the x86_64 architecture with the RedHat 7.0 operating system.
Execute the hammer os add-architecture command to do this.
# hammer os add-architecture --architecture x86_64 --id OS_ID

The appropriate partition table needs to be associated with the operating system.
Use the hammer os add-ptable command to associate the partition table to the operating system Id.
# hammer os add-ptable --ptable-id P_ID --id OS_ID

## Configure Subnets
A subnet called OpenStack was created automatically during installation. Execute hammer subnet list and note the ID of this subnet.
# hammer subnet list

IP addresses can be automatically assigned to newly provisioned hosts from this subnet. To do this, a range of IPs to assign must be defined.
Use the hammer subnet update command to assign the range of IP addresses and to also set the default gateway for the provisioned hosts.
If the foreman server is acting as the gateway, the gateway address is the IP address of the Foreman servers provisioning interface.
# hammer subnet update --id SN_ID --from START_IP_RANGE --to END_IP_RANGE \
 --gateway GATEWAY_IP

## Configure Templates
Four template files are provided and used to provision hosts.
dell-osp-ks.template	Provisioning template that provides the kickstart file.
dell-osp-pxe.template	PXE template that contains the PXE configuration..
interface_config.template	Snippet that provides a means to configure extra interfaces during installation. This template is called from the kickstart template.
bonding_snippet.template	Snippet that provides a means to bond interfaces during installation. This template is called from the kickstart template.

Create the templates using the hammer template create command.
# hammer template create --name "Dell OpenStack Kickstart Template" --type provision \
 --operatingsystem-ids "OS_ID_RH7.0" --file /root/pilot/dell-osp-ks.template
# hammer template create --name "Dell OpenStack PXE Template" --type PXELinux \
 --operatingsystem-ids "OS_ID_RH7.0" --file /root/pilot/dell-osp-pxe.template
# hammer template create --name "bond_interfaces" --type snippet \
 --file /root/pilot/bonding_snippet.template
# hammer template create --name "interface_config" --type snippet \
 --file /root/pilot/interface_config.template

After the templates are created, use the hammer template list command to determine the IDs of the templates.

The provisioning and PXE templates must be associated with the operating systems. Use the hammer os update command to update the template associations.
Execute the following command for the RedHat 7.0 operating system ID. This command also associates the installation medium to the operating system.
# hammer os update --config-template-ids "KS_ID, PXE_ID" \
 --medium-ids MEDIUM_ID --id OS_ID

The templates are now associated with the operating system, they must now be set as the default templates for the operating systems.
Execute the hammer os set-default template command for the provisioning and PXELinux templates. The command will be executed two times.
# hammer os set-default-template --config-template-id TMPLT_ID --id OS_ID

The hammer os info command can be used to check the configuration of the operating systems.
# hammer os info --id 1
Id: 1
Full name: RedHat 7.0
Release name:
Family: Redhat
Name: RedHat
Major version: 7
Minor version: 0
Partition tables:
Default templates:
   Dell OpenStack Kickstart Template (provision)
   Dell OpenStack PXE Template (PXELinux)
Architectures:
Installation media:
   Red Hat Satellite
Templates:
   Dell OpenStack Kickstart Template (provision)
   Dell OpenStack PXE Template (PXELinux)
Parameters:

## Gather More Information
A few more IDs are required in order to install a host. Execute the following commands and take note of the appropriate IDs.
- Environments
  # hammer environment list
- Domains
  # hammer domain list
- Puppet Proxy
  # hammer proxy list
- Architectures
  # hammer architecture list
## Configure facts updates
Foreman updates the host information using the Puppet facts. Foreman updates the provisioning information with the first interface returned from the Puppet facts. To prevent this, perform the following steps.
- Log into the Foreman UI.
- Select the Administer drop down on the top right of the window.
- Select Settings. Select the Provisioning tab.
- Edit the ignore_puppet_facts_for_provisioning setting and set it to true.

## Configure the Operating System for Updates.
Configure the Operating system definition with the parameters for registering the provisioned host for updates.
The hammer os set-parameter command is used to set the parameters.
The following parameters are set.
subscription_manager	Specifies that the hosts will register with Subscription Manager. (true or false)
subscription_manager_username	The username of the Subscription Manager account to register to.
subscription_manager_password	The password for the Subscription Manager account.

Define the OS_ID variable to the ID of the operating system then execute the remaining commands.
Make sure to specify the appropriate username, password, and pool ID by replacing the CHANGEME's and POOL_ID.
# OS_ID=2
# hammer os set-parameter --operatingsystem-id ${OS_ID} \
 --name subscription_manager --value true
# hammer os set-parameter --operatingsystem-id ${OS_ID} \
 --name subscription_manager_username --value CHANGEME
# hammer os set-parameter --operatingsystem-id ${OS_ID} \
 --name subscription_manager_password --value 'CHANGEME'

### Optional Proxy Settings
Proxy settings for the subscription-manager and yum commands can be set by defining the needed parameters. These parameters are completely optional if not needed.
Although defining and using the following parameters will work for most environments, they may not work for all. Setting the parameters gives the provisioning template the information to set the proxy information using the subscription-manager config command.
If these setting do not work in your environment, the kickstart file may need to be manually modified. This can be done using the Foreman user interface..
The following parameters can be set using the hammer os set-parameter command as above.
subscription_manager_proxy	The proxy server to use, if needed.
subscription_manager_proxy_port	The proxy port to use, if needed.
subscription_manager_proxy_user	The proxy username, if needed.
subscription_manager_proxy_password	The proxy password, if needed.

# Provisioning the Nodes
Provision the nodes using the following command. Variables are being used to make it easier to use the hammer command.
Simply set the NAME, PTABLE, and MAC variables appropriately for a host, then execute the hammer host create command. Once the host is created, reset the variables for the next host and execute the same hammer command again.
Repeat this until all hosts are created. Make sure to change the root password on the command line as needed.
NAME	The hostname of the provisioned host.
PTABLE	The ID of the partition table that should be used when deploying this host. This ID is the same for all the compute nodes, but the controller uses a different partition tablei ID.
MAC	The hardware address of the provisioning interface for the node.

Change the remaining IDs in the command as appropriate.
# NAME=CHANGEME
# PTABLE=CHANGEME
# MAC=CHANGEME
# hammer host create --name "${NAME}" --root-password 'CHANGEME' \
   --build true --enabled true --managed true --environment-id 2 \
   --domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 2 \
   --subnet-id 1 --architecture-id 1 --medium-id 9 \
   --partition-table-id ${PTABLE} \
   --mac ${MAC}

## Get host information
The IDs of the newly defined hosts are needed to finish their configuration.
Execute the hammer host list command to get the host IDs. Take note of these IDs.
# hammer host list

## Controller Node
The controller nodes have two bonded interfaces, one with two vlans configured, and two remaining interfaces that are not bonded. The Public API network is on a pair of bonded interfaces and the Private API and Storage networks are on a separate pair of bonded interfaces.
The Private API and Storage networks are VLAN tagged networks on a bonded interface. The Provisioning and the Management interfaces are on individual non-bonded interfaces.
### Non-Bonded Nic Configuration
The nics parameter can be set on the hosts to provide the information needed to allow the kickstart file to configure the non-bonded interfaces.
Set the nics parameter on the controller host to configure the non-bonded interfaces. The Provisioning interface is configured by Foreman, so it does not need to be configured again.
The value for the nic parameter consists of a space separated list of key=value pairs. Each pair contains the configuration information for a single nic. This list is entered in the same format a s a bash associative array. The entire value is enclosed within single tick marks and parentheses. '( …)'
Each key/value is in the following format:
[IFACE]="parameters"
An example of defining a single interface:
# hammer host set-parameter --host-id 3 --name nics \
 --value '([em1]="onboot static aa:bb:cc:dd:ee:ff 192.168.0.110/255.255.255.0")'

The parameters consist of the following:
onboot	The interface is enabled when the system boots. Default is disabled.
dhcp | static | none	The interface gets its network configuration using DHCP,· the network configuration is statically configured, or the interface has no network configuration. If no option is specified, dhcp is assumed.
xx:xx:xx:xx:xx:xx	The hardware address of the interface.
x.x.x.x/y.y.y.y	The IP address and Network mask of the interface. Used only when static is specified. Must be in the format presented.

Execute the following command to set the nic parameters for the two other interfaces used by the controller node. Replace the HOST_ID, IFACE, MAC, and IP/MASK parameters as appropriate.
# hammer host set-parameter --host-id HOST_ID --name nics \
 --value '([IFACE]="onboot static MAC IP/MASK" [IFACE]="onboot static MAC IP/MASK")'

### Bonded Nic Configuration
Three parameters can be set on the hosts to provide the information needed to allow the kickstart file to configure the bonded interfaces. These parameters are: bonds, bond_ifaces, and bond_opts.

The bonds parameter is similar to the nics parameter used earlier with the addition of the vlan option and the removal of the mac address option.
When creating a VLAN tagged bond, use the vlan option to let the bonding_snippet know this bond is vlan tagged. Also specify the tag number in the bond name.
For example:
'( [bond0]="onboot none" [bond0.301]="onboot static vlan 172.30.139.62/255.255.255.0" )'

Created a bond0 that is enabled at boot. It then creates a VLAN tagged bond on the bond called bond0.301.
See the documentation on the bonding_snippit for more information.

The bond_ifaces parameter is used to specify the interfaces for each bond.
For example:
'( [bond0]="em1 em2" )'

Bonds interfaces em1 and em2 into bond0.

The bond_opts parameter specifies the bonding options to use for each bond.
For example:
'( "[bond0]="mode=active-passive" )'

Create the three needed parameters using the hammer host set-parameter command. Replace the HOST_ID, VLAN, and IP/MASK information as appropriate to define the bonds.
# hammer host set-parameter --host-id HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.VLAN1]="onboot static vlan IP/MASK"
 [bond0.VLAN2]="onboot static vlan IP/MASK" [bond1]="onboot static IP/MASK")'
# hammer host set-parameter --host-id HOST_ID --name bond_ifaces \
 --value '( [bond0]="p3p1 p3p2" [bond1]="em1 em2")'
# hammer host set-parameter --host-id HOST_ID --name bond_opts \
 --value '( [bond0]="mode=active-backup" [bond1]="mode=active-backup")'

Repeat the parameter configuration for all the controller nodes.
## Compute Nodes
The compute nodes have two separate bonds and a single non-bonded interface for its networking. The single interface is connects to the Provisioning network and is already configured.
One bond connects to the Nova Public Network, while the other bond connects to the Nova Private, Private_API, and Storage networks. Each network on the second bond are VLAN tagged.
Set the bonds, bond_ifaces, and bond_opts parameters for each compute node.
Make sure the bond_opts sets the MODE to balance-tlb and PROMISC to yes.
An example set of commands follows.
# hammer host set-parameter --host-id HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.300]="onboot static vlan 172.20.139.110/255.255.255.0"
 [bond0.301]="onboot static vlan 172.30.139.110/255.255.255.0"
 [bond0.302]="onboot static vlan 172.40.139.110/255.255.255.0"
 [bond1]="onboot static 172.10.139.61/255.255.255.0")'
# hammer host set-parameter --host-id HOST_ID --name bond_ifaces \
 --value '( [bond0]="p3p1 p3p2" [bond1]="em1 em2")'
# hammer host set-parameter --host-id HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb PROMISC=yes" [bond1]="mode=balance-tlb PROMISC=yes")'

## Set Host Update Parameters
Each node can use a separate pool ID and require different repositories. These parameters are set on a per host basis instead of an operating system.
The following parameters need to be set on each host.
subscription_manager_pool	The ID of the pool to attach the host to.
subscription_manager_repos	The repositories that should be enabled after the host is registered.

### Determine Pool ID
To determine the pool id, you must have an existing server that is registered to the RedHat Hosted Services. This server must also be registered using the same credentials as the ones being used in this environment.
Once the server is correctly registered, execute the subscription-manager list --all --available command to see the available subscription pools.
The command will output a list of available pools. Each section of information lists what the subscription provides, its pool ID, how many are available, the type of system it is for, as well as other information.

Determine the correct pool ID needed for this environment and take note of it. Place close attention to the System Type. The System Type can be Virtual or Physical. You cannot use a pool marked as Virtual for a physical server.
# subscription-manager list --all --available
[OUTPUT ABBREVIATED]
Subscription Name: Red Hat Cloud Infrastructure, Standard (8-sockets)
Provides: Red Hat Beta
        Red Hat OpenStack Beta
        JBoss Enterprise Application Platform
        Red Hat Software Collections (for RHEL Server)
        Red Hat Enterprise Virtualization
        Oracle Java (for RHEL Server)
        Red Hat OpenStack
        Red Hat Enterprise MRG Messaging
        Red Hat Enterprise Linux Server
        Red Hat Enterprise Linux High Availability (for RHEL Server)
        Red Hat Software Collections Beta (for RHEL Server)
        Red Hat Enterprise Linux Load Balancer (for RHEL Server)
        Red Hat CloudForms
SKU: MCT2861
Pool ID: aaaa111bbb222ccc333ddd444eee5556
Available: 7
Suggested: 1
Service Level: Standard
Service Type: L1-L3
Multi-Entitlement: No
Ends: 09/23/2015
System Type: Physical
[OUTPUT ABBREVIATED]

### Configure the Pool ID
Execute the following command for each host. Substitute the HOST_ID and POOL_ID as appropriate.
# hammer host set-parameter --host-id-id HOST_ID \
 --name subscription_manager_pool --value POOL_ID

### Configure the Repositories
The controller nodes and compute nodes both require the rhel-server-rhscl-7-rpms, rhel-7-server-rpms, and rhel-7-server-openstack-5.0-rpms, repositories.

Execute the following command on each controller node to enable the needed repositories.
# hammer os set-parameter --host-id HOST_ID --name subscription_manager_repos \
   --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
   rhel-7-server-openstack-5.0-rpms,rhel-ha-for-rhel-7-server-rpms"

The controller nodes also require the rhel-ha-for-rhel-7-server-rpms repository.
Execute the following command on each compute node to enable the needed repositories.
# hammer os set-parameter --host-id HOST_ID --name subscription_manager_repos \
   --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
   rhel-7-server-openstack-5.0-rpms"

## Start Provisioning
PXE boot each of the nodes. After they are booted, make sure the networks are configured appropriately.
## Ceph Deployment
If Ceph must be configured on these nodes, follow the Red Hat Openstack Platform Integration with Ceph document.
## Next Steps
After the Ceph configuration is complete or if Ceph configuration is not needed, continue the configuration using the Dell Pilot Hostgroups Deployment document.

# Appendix - Example Hammer Commands
hammer-list
hammer medium create --name "Dell OSP Pilot" --os-family RedHat \
 --path 'http://rh6fore.r5.lab/ks/dist/ks-rhel-$arch-server-$majo-$version'
hammer medium list
hammer partition-table create
hammer partition-table create --name dell-pilot --os-family Redhat --file dell-pilo.partition
hammer partition-table create --name dell-pilot --os-family Redhat --file dell-pilot.partition
hammer partition-table create --name dell-pilot --os-family Redhat --file dell-pilot.partition
hammer os create --name "RedHat" --major 7 --minor 0 --family Redhat
hammer os list
hammer os add-architecture --architecture x86_64 --id 3
hammer os add-ptable --ptable-id 8 --id 3
hammer subnet list
hammer template create --name "Dell OpenStack Kickstart Template" --type provision \
hammer template create --name "Dell OpenStack Kickstart Template" \
 --operatingsystem-ids "3" --file dell-osp-ks.template
hammer template create --name "Dell OpenStack Kickstart Template" type provision \
 --operatingsystem-ids "3" --file dell-osp-ks.template
hammer template create --name "Dell OpenStack Kickstart Template" --type provision \
 --operatingsystem-ids "3" --file dell-osp-ks.template
hammer template create --name "Dell OpenStack PXE Template" --type PXELinux \
 --operatingsystem-ids "3" --file dell-osp-pxe.template
hammer template create --name "bond_interfaces" --type snippet \
hammer template create --name "bond_interfaces" --type snippet--file bonding_snippet.template
hammer template create --name "bond_interfaces" --type snippet --file bonding_snippet.template
hammer template create --name "interface_config" --type snippet --file interface_config.template
hammer tempalte list
hammer template list
hammer os update --config-template-ids "33,34" --medium-ids 8 --id 3
hammer os set-default-template --config-template-id 34 --id 3
hammer os info --id 3
hammer domain list
hammer proxy list
hammer architecture list
hammer os set-parameter
hammer os set-parameter --operatingsystem-id
hammer os list
hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager --value true
hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager --value true
hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager --value true
hammer os set-parameter --operatingsystem-id 3 \
 --name subscription_manager --value true
hammer os set-parameter --operatingsystem-id 3 \
 --name subscription_manager_username --value dellcloudsol
hammer os set-parameter --operatingsystem-id 3 \
 --name subscription_manager_password --value cr0wBar!
hammer os list

hammer-nic-bond-cntl1
HOST_ID='15'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name nics \
 --value '([em2]="onboot static 192.168.110.127/255.255.255.0")'
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.130/255.255.255.0"
 [bond0]="onboot none" [bond0.140]="onboot static vlan 192.168.123.41/255.255.255.0"
 [bond1]="onboot static 10.9.244.130/255.255.254.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p5p2 p7p2" [bond1]="p5p1 p7p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-cntl2
HOST_ID='16'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name nics \
 --value '([em2]="onboot static 192.168.110.128/255.255.255.0")'
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.131/255.255.255.0"
 [bond0]="onboot none" [bond0.140]="onboot static vlan 192.168.123.42/255.255.255.0"
 [bond1]="onboot static 10.9.244.131/255.255.254.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p5p2 p7p2" [bond1]="p5p1 p7p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-cntl3
HOST_ID='21'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name nics \
 --value '([em2]="onboot static 192.168.110.129/255.255.255.0")'
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.132/255.255.255.0"
 [bond0]="onboot none" [bond0.140]="onboot static vlan 192.168.123.43/255.255.255.0"
 [bond1]="onboot static 10.9.244.132/255.255.254.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p5p2 p6p2" [bond1]="p5p1 p6p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-nova1
HOST_ID='24'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.133/255.255.255.0"
 [bond0]="onboot none" [bond0.130]="onboot static vlan 192.168.130.133/255.255.255.0"
 [bond0]="onboot none" [bond0.140]="onboot static vlan 192.168.123.44/255.255.255.0"
 [bond1]="onboot none" [bond1.207]="onboot static vlan 192.168.207.133/255.255.255.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p5p2 p6p2" [bond1]="p5p1 p6p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-nova2
HOST_ID='25'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.134/255.255.255.0"
 [bond0]="onboot none" [bond0.130]="onboot static vlan 192.168.130.134/255.255.255.0"
 [bond0]="onboot none" [bond0.140]="onboot static vlan 192.168.123.45/255.255.255.0"
 [bond1]="onboot none" [bond1.207]="onboot static vlan 192.168.207.134/255.255.255.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p5p2 p6p2" [bond1]="p5p1 p6p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-nova3
HOST_ID='26'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.135/255.255.255.0"
 [bond0]="onboot none" [bond0.130]="onboot static vlan 192.168.130.135/255.255.255.0"
 [bond0]="onboot none" [bond0.140]="onboot static vlan 192.168.123.46/255.255.255.0"
 [bond1]="onboot none" [bond1.207]="onboot static vlan 192.168.207.135/255.255.255.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p1p2 p5p2" [bond1]="p1p1 p5p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-ceph1
HOST_ID='28'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.140/255.255.255.0"
 [bond1]="onboot none" [bond1.191]="onboot static vlan 192.168.191.140/255.255.255.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p4p2 p6p2" [bond1]="p4p1 p6p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-ceph2
HOST_ID='29'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.141/255.255.255.0"
 [bond1]="onboot none" [bond1.191]="onboot static vlan 192.168.191.141/255.255.255.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p4p2 p6p2" [bond1]="p4p1 p6p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-nic-bond-ceph3
HOST_ID='30'
POOLID=8a85f98744091dea0144314ba24c726c
hammer host set-parameter --host-id $HOST_ID --name bonds \
 --value '( [bond0]="onboot none" [bond0.190]="onboot static vlan 192.168.190.142/255.255.255.0"
 [bond1]="onboot none" [bond1.191]="onboot static vlan 192.168.191.142/255.255.255.0" )'
hammer host set-parameter --host-id $HOST_ID --name bond_opts \
 --value '( [bond0]="mode=balance-tlb miimon=100" [bond1]="mode=balance-tlb miimon=100" )'
hammer host set-parameter --host-id $HOST_ID --name bond_ifaces \
 --value '([bond0]="p4p2 p6p2" [bond1]="p4p1 p6p1" ) '
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy \
 --value "proxy.us.dell.com"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_proxy_port \
 --value "80"
hammer host set-parameter --host-id ${HOST_ID} --name subscription_manager_pool \
 --value "${POOLID}"
hammer host set-parameter --host-id $HOST_ID --name subscription_manager_repos \
 --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms,
 rhel-7-server-openstack-5.0-rpms, rhel-ha-for-rhel-7-server-rpms"

hammer-deploy-cntl1
NAME=rh7cntl1
PTABLE=12
MAC=B8:CA:3A:68:67:54
IP=192.168.119.130
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-cntl2
NAME=rh7cntl2
PTABLE=12
MAC=B8:CA:3A:68:67:68
IP=192.168.119.131
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-cntl3
NAME=rh7cntl3
PTABLE=12
MAC=B8:CA:3A:67:43:6C
IP=192.168.119.132
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-nova1
NAME=rh7nova1
PTABLE=12
MAC=B8:CA:3A:67:3C:D0
IP=192.168.119.133
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-nova2
NAME=rh7nova2
PTABLE=12
MAC=B8:CA:3A:67:3F:68
IP=192.168.119.134
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-nova3
NAME=rh7nova3
PTABLE=12
MAC=B8:CA:3A:67:3D:C8
IP=192.168.119.135
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-ceph1
NAME=rh7ss1
PTABLE=12
MAC=B8:CA:3A:67:17:4C
IP=192.168.119.140
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-ceph2
NAME=rh7ss2
PTABLE=12
MAC=B8:CA:3A:67:0C:7C
IP=192.168.119.141
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}

hammer-deploy-ceph3
NAME=rh7ss3
PTABLE=12
MAC=B8:CA:3A:67:0D:38
IP=192.168.119.142
hammer host create --name "${NAME}" --root-password 'cr0wBar!' \
--build true --enabled true --managed true --environment-id 2 \
--domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 3 --ip ${IP} \
--subnet-id 1 --architecture-id 1 --medium-id 9 --partition-table-id ${PTABLE} --mac ${MAC}
hammer host list |grep ${NAME}