Dell Proof of Concept Deployment Guide

# Configure Foreman Server
If the provisioning interface on the provisioned host is not the first interface returned in the puppet data, Foreman will overwrite the configuration in the database. This can cause issues later.
To prevent Foreman from changing the IP and MAC information to reflect the puppet data, change the ignore_puppet_facts_for_provisioning setting.
- Log into the Foreman user interface.
- Move the mouse over the Administer drop down menu on the right side of the interface.
- Select Settings from the menu.
- Select the Provisioning tab.
- Select Value for the ignore_puppet_facts_for_provisioning setting.
  - Change this setting to true.
## Hammer Command Preparation
During the steps in this document, the hammer command is used to more easily perform the configurations. Usage of the hammer command requires identifiers for the various pieces of information stored within the Foreman server. This includes identifiers for the defined installation media, partitions, templates, hosts, as well as other items.
A checklist file, dell-poc-checklist.pdf, is available to easily keep track of this information.
Download and print the Dell POC Checklist from https://wiki.opencrowbar.org/pages/viewpage.action?pageId=6326050.
Write the various information gathered and needed on the checklist for reference as needed.
Several steps in this document use files to configure the environment. These files are available in a TAR file called dell-poc-deploy.tgz. This TAR file is available from https://wiki.opencrowbar.org/pages/viewpage.action?pageId=6326050.
Download the tar file and unzip it into the /root/poc directory..
# mkdir /root/poc
# cd /root/poc
# tar xzvf /PATH/TO/FILE/dell-poc-deploy.tgz

## Version Locking
Execute the following command to make the version locking files available during node provisioning:
# cp -r /root/poc/vlock_files /usr/share/foreman/public
## The Hammer Command
- Install the packages that contain the hammer command.
  # yum -y install "*hammer*"
  This should install the following packages:
  - rubygem-hammer_cli-doc-0.1.1-12.el6sat.noarch
  - rubygem-hammer_cli-0.1.1-12.el6sat.noarch
  - rubygem-hammer_cli_foreman-0.1.1-16.el6sat.noarch
  - rubygem-hammer_cli_foreman-doc-0.1.1-16.el6sat.noarch
- Configure the hammer command to display 200 items per page. This just makes it easier to read everything.
  - Replace the value for the :per_page: option in the /etc/hammer/cli_config.yml file.
- Configure the hammer command to not prompt for a username/password when connecting.
  - Add the following to the beginning of the /etc/hammer/cli_config.yml file. Replace the name and password appropriately.
    :foreman:
    :username: 'admin'
    :password: 'changeme'
## Hammer help
The hammer command takes the --help option. This option can be used with most of its sub-commands as well. It is useful to see the various options that can be used.
## Configure the Installation Medium
Configure the installation medium that will be used to provision the hosts.
Use the hammer medium create command to add the entry.
The command requires the --name, --os-family and --path options.
The name option should specify a name that is appropriate for the installation.
The os-family should remain Redhat in most cases.
The path option specifies the path or URL to the installation tree.
### Satellite Server
The path included in the example below should work with most satellite installation, just replace SATELLITE_SERVER with the appropriate FQDN.
# hammer medium create --name "Dell OSP Pilot" --os-family Redhat \
 --path 'http://SATELLITE_SERVER/ks/dist/ks-rhel-$arch-server-$major-$version'
### Local ISO on Foreman Node
- mkdir /usr/share/foreman/public/iso
- Copy the RHEL7 iso to the /root directory of the foreman node
- Edit /etc/fstab
- Add the following line to the end:
  /root/RHEL-7.0-Server-x86_64-dvd.iso /usr/share/foreman/public/iso iso9660 loop,ro 0 0
- mount -a
hammer medium create --name "Dell OSP Pilot" --os-family Redhat \
 --path 'http://FOREMAN_SERVER/iso'
### Local ISO on Solution Admin Host
- On the Solution Admin Host:
  - yum install httpd
  - Configure httpd with any options you want. Defaults will work, but are not secure.
  - copy the ISO to the SAH in /store/data/iso
  - "mount -o loop ISO NAME /mnt"
  - "mkdir /store/data/iso/RHEL6.5" (Name of the OS)
  - "rsync -av /mnt/ /store/data/iso/RHEL6.5"
  - "umount /mnt"
  - "ln -s /store/data/iso/RHEL6.5 RHEL6.5"
- Validate the web interface works
  http://ipaddress of foreman/RHEL6.5/README
## Note the Medium ID
After the medium is created, execute the hammer medium list command.
Take note of the ID (first column) for the newly created medium. This will be needed later.
## Configure the Partition Tables
Configure the partition tables that the provisioned hosts will use. These partition tables are provided in two files.
dell-poc-controller.partition	Partition table for the POC controller nodes.
dell-poc-compute.partition	Partition table for the POC compute nodes.

Use the hammer partition-table create command to install the partition tables. Specify an appropriate NAME for each partition table and specify the file that contains the data. Install only the needed partition tables.
# hammer partition-table create --name dell-poc-controller --os-family Redhat \
 --file /root/poc/dell-poc-controller.partition
# hammer partition-table create --name dell-poc-compute --os-family Redhat \
 --file /root/poc/dell-poc-compute.partition

After the partition tables are created, execute the hammer partition-table list command.
Take note of the ID’s of the newly created partition tables.
## Configure the Operating Systems
A operating system definition for Red Hat Enterprise Linux 6.5 was created when the Foreman server registered with itself. But a definition for Red Hat Enterprise Linux 7.0 was not.
Create a new operating system definition for Red Hat Enterprise Linux 7.0.
Use the hammer os create command to create the definition.
# hammer os create --name "RedHat" --major 7 --minor 0 --family Redhat
After creating the operating system, execute the hammer os list command.
Take note of the ID’s for the new RedHat 6.5 and RedHat 7.0 operating systems.
Associate the x86_64 architecture with the RedHat 6.5 and RedHat 7.0 operating systems.
Execute the hammer os add-architecture command for each operating systems ID.
# hammer os add-architecture --architecture x86_64 --id RHEL6.5_OS_ID
# hammer os add-architecture --architecture x86_64 --id RHEL7.0_OS_ID

The appropriate partition tables need associated with the operating systems.
Use the hammer os add-ptable command to associate the appropriate partition tables to the operating system Id.
This command must be executed four times, once for each combination of partition table and the RedHat 6.5 and RedHat 7.0 operating system IDs.
# hammer os add-ptable --ptable-id P_ID --id OS_ID

## Configure Subnets
A subnet called OpenStack was created automatically during installation. Execute hammer subnet list and note the ID of this subnet.
# hammer subnet list

IP addresses can be automatically assigned to newly provisioned hosts from this subnet. To do this, a range of IPs to assign must be defined.
Use the hammer subnet update command to assign the range of IP addresses and to also set the default gateway for the provisioned hosts.
If the foreman server is acting as the gateway, the gateway address is the IP address of the Foreman servers provisioning interface.
# hammer subnet update --id SN_ID --from START_IP_RANGE --to END_IP_RANGE \
 --gateway GATEWAY_IP

## Configure Templates
Four template files are provided and used to provision hosts.
dell-osp-ks.template	Provisioning template that provides the kickstart file.
dell-osp-pxe.template	PXE template that contains the PXE configuration..
interface_config.template	Snippet that provides a means to configure extra interfaces during installation. This template is called from the kickstart template.
bonding_snippet.template	Snippet that provides a means to bond interfaces during installation. This template is called from the kickstart template.

Create the templates using the hammer template create command.
# hammer template create --name "Dell OpenStack Kickstart Template" --type provision \
 --operatingsystem-ids "OS_ID_RH6.5, OS_ID_RH7.0" --file /root/poc/dell-osp-ks.template
# hammer template create --name "Dell OpenStack PXE Template" --type PXELinux \
 --operatingsystem-ids "OS_ID_RH6.5, OS_ID_RH7.0" --file /root/poc/dell-osp-pxe.template
# hammer template create --name "bond_interfaces" --type snippet \
 --file /root/poc/bonding_snippet.template
# hammer template create --name "interface_config" --type snippet \
 --file /root/poc/interface_config.template

After the templates are created, use the hammer template list command to determine the IDs of the templates.

The provisioning and PXE templates must be associated with the operating systems. Use the hammer os update command to update the template associations.
Execute the following command for each of the RedHat 6.5 and RedHat 7.0 IDs. This command also associates the installation medium to the operating system.
# hammer os update --config-template-ids "KS_ID, PXE_ID" \
 --medium-ids MEDIUM_ID --id OS_ID

The templates are now associated with the operating systems, they must now be set as the default templates for the operating systems.
Execute the hammer os set-default template command for each template and operating system combination. The command should be executed four times in total.
# hammer os set-default-template --config-template-id TMPLT_ID --id OS_ID

The hammer os info command can be used to check the configuration of the operating systems.
# hammer os info --id 1
Id: 1
Full name: RedHat 6.5
Release name:
Family: Redhat
Name: RedHat
Major version: 6
Minor version: 5
Partition tables:
Default templates:
   Dell OpenStack Kickstart Template (provision)
   Dell OpenStack PXE Template (PXELinux)
Architectures:
Installation media:
   Red Hat Satellite
Templates:
   Dell OpenStack Kickstart Template (provision)
   Dell OpenStack PXE Template (PXELinux)
Parameters:

## Gather More Information
A few more IDs are required in order to install a host. Execute the following commands and take note of the apropriate IDs.
- Environments
  # hammer environment list
- Domains
  # hammer domain list
- Puppet Proxy
  # hammer proxy list
- Architectures
  # hammer architecture list
## Configure facts updates
Foreman updates the host information using the Puppet facts. Foreman updates the provisioning information with the first interface returned from the Puppet facts. To prevent this, perform the following steps.
- Log into the Foreman UI.
- Select the Administer drop down on the top right of the window.
- Select Settings. Select the Provisioning tab.
- Edit the ignore_puppet_facts_for_provisioning setting and set it to true.

# Provisioning the Nodes
Provision the nodes using the following command. Variables are being used to make it easier to use the hammer command.
Simply set the NAME, PTABLE, and MAC variables appropriately for a host, then execute the hammer host create command. Once the host is created, reset the variables for the next host and execute the same hammer command again.
Repeat this until all hosts are created. Make sure to change the root password on the command line as needed.
NAME	The host name of the provisioned host.
PTABLE	The ID of the partition table that should be used when deploying this host. This ID is the same for all the compute nodes, but the controller uses a different partition table ID.
MAC	The hardware address of the provisioning interface for the node.

Change the remaining IDs in the command as appropriate.
# NAME=CHANGEME
# PTABLE=CHANGEME
# MAC=CHANGEME
# hammer host create --name "${NAME}" --root-password 'CHANGEME' \
   --build true --enabled true --managed true --environment-id 2 \
   --domain-id 1 --puppet-proxy-id 1 --operatingsystem-id 2 \
   --subnet-id 1 --architecture-id 1 --medium-id 9 \
   --partition-table-id ${PTABLE} \
   --mac ${MAC}

## Get host information
The IDs of the newly defined hosts are needed to finish their configuration.
Execute the hammer host list command to get the host IDs. Take note of these IDs.
# hammer host list

## Configure Operating System Updates.
Configure the Operating system definition with the parameters for registering the provisioned host for updates.
The hammer os set-parameter command is used to set the parameters.
The following parameters are set.
subscription_manager	Specifies that the hosts will register with Subscription Manager. (true or false)
subscription_manager_username	The user name of the Subscription Manager account to register to.
subscription_manager_password	The password for the Subscription Manager account.
subscription_manager_pool	The ID of the pool to attach the host to.
subscription_manager_repos	The repositories that should be enabled after the host is registered.

### Determine Pool ID
To determine the pool id, you must have an existing server that is registered to the RedHat Hosted Services. This server must also be registered using the same credentials as the ones being used in this environment.
Once the server is correctly registered, execute the subscription-manager list --all --available command to see the available subscription pools.
The command will output a list of available pools. Each section of information lists what the subscription provides, its pool ID, how many are available, the type of system it is for, as well as other information.

Determine the correct pool ID needed for this environment and take note of it. Place close attention to the System Type. The System Type can be Virtual or Physical. You cannot use a pool marked as Virtual for a physical server.
# subscription-manager list --all --available
[OUTPUT ABBREVIATED]
Subscription Name: Red Hat Cloud Infrastructure, Standard (8-sockets)
Provides: Red Hat Beta
        Red Hat OpenStack Beta
        JBoss Enterprise Application Platform
        Red Hat Software Collections (for RHEL Server)
        Red Hat Enterprise Virtualization
        Oracle Java (for RHEL Server)
        Red Hat OpenStack
        Red Hat Enterprise MRG Messaging
        Red Hat Enterprise Linux Server
        Red Hat Enterprise Linux High Availability (for RHEL Server)
        Red Hat Software Collections Beta (for RHEL Server)
        Red Hat Enterprise Linux Load Balancer (for RHEL Server)
        Red Hat CloudForms
SKU: MCT2861
Pool ID: aaaa111bbb222ccc333ddd444eee5556
Available: 7
Suggested: 1
Service Level: Standard
Service Type: L1-L3
Multi-Entitlement: No
Ends: 09/23/2015
System Type: Physical
[OUTPUT ABBREVIATED]

These steps should be performed for both the RedHat 6.5 and RedHat 7.0 operating systems. Define the OS_ID variable to the ID of the operating system then execute the remaining commands.
Change the OS_ID to the other ID and repeat the commands again.

Make sure to specify the appropriate username, password, and pool ID by replacing the CHANGEME's and POOL_ID.
# OS_ID=2
# hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager --value true
# hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager_username --value CHANGEME
# hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager_password --value 'CHANGEME'
# hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager_pool --value POOL_ID
# hammer os set-parameter --operatingsystem-id ${OS_ID} --name subscription_manager_repos \
   --value "rhel-server-rhscl-7-rpms, rhel-7-server-rpms, rhel-7-server-openstack-5.0-rpms"

### Optional Proxy Settings
Proxy settings for the subscription-manager and yum commands can be set by defining the needed parameters. These parameters are completely optional if not needed.
Although defining and using the following parameters will work for most environments, they may not work for all. Setting the parameters gives the provisioning template the information to set the proxy information using the subscription-manager config command.
If these setting do not work in your environment, the kickstart file may need to be manually modified. This can be done using the Foreman user interface..
The following parameters can be set using the hammer os set-parameter command as above.
subscription_manager_proxy	The proxy server to use, if needed.
subscription_manager_proxy_port	The proxy port to use, if needed.
subscription_manager_proxy_user	The proxy username, if needed.
subscription_manager_proxy_password	The proxy password, if needed.

## Controller Node
Set nics parameter on the controller host. This provides the kickstart file the needed information to configure the two non-provisioned (Public API, Private API) interfaces.
The value for the parameter consists of a space separated list of nic configuration bash associative array. The entire value is enclosed within single tick-marks and parentheses. ( …)
Each key/value is in the following format: [IFACE]="parameters"
An example of defining two interfaces: hammer host set-parameter --host-id 3 --name nics \ --value ([em1]="onboot static aa:bb:cc:dd:ee:ff 192.168.0.110/255.255.255.0" [em2]="onboot static 11:22:33:44:55:66 192.169.10.110/255.255.255.0")
The parameters consist of the following:
onboot	The interface is enabled when the system boots. Default is disabled.
dhcp | static | none	The interface gets its network configuration using DHCP,· the network configuration is staticaly configured, or the interface has no network configuration. If no option is specified, dhcp is assumed.
xx:xx:xx:xx:xx:xx	The hardware address of the interface.
x.x.x.x/y.y.y.y	The IP address and Network mask of the interface. Used only when static is specified. Must be in the format presented.

Execute the following command to set the nic parameters for the two other interfaces used by the controller node. Replace the HOST_ID, IFACE, MAC, and IP/MASK parameters as appropriate.
# hammer host set-parameter --host-id HOST_ID --name nics \
 --value '([IFACE]="onboot static MAC IP/MASK" [IFACE]="onboot static MAC IP/MASK")'

Execute the following command to make the RPM version locking file available during provisioning. Replace HOST_ID with the host ID and FOREMAN_SERVER with the IP address of the Foreman server on the provisioning network.
# hammer host set-parameter --host-id HOST_ID --name yum_versionlock_file \
 --value 'https://FOREMAN_SERVER/vlock_files/versionlock.list_cntl'

## Compute Nodes
The nics parameter must be set to configure the three remaining ( Nova Public, Nova Private, Private API) interfaces used on the compute nodes.
Execute the following hammer command on each compute node. Note that the third interface specified is the IFACE_NOVA_PRIVATE interface. This interface has no network configuration, but should be enabled upon boot.
# hammer host set-parameter --host-id HOST_ID --name nics \
 --value '([IFACE]="onboot static MAC IP/MASK" [IFACE]="onboot static MAC IP/MASK"
[IFACE_NOVA_PRIVATE]="onboot none MAC")'

Execute the following command to make the RPM version locking file available during provisioning. Replace HOST_ID with the host ID and FOREMAN_SERVER with the IP address of the Foreman server on the provisioning network.
# hammer host set-parameter --host-id HOST_ID --name yum_versionlock_file \
 --value 'https://FOREMAN_SERVER/vlock_files/versionlock.list_nova'

## Start Provisioning
PXE boot each of the nodes. After they are booted, make sure the networks are configured appropriately.
# Assigning Hostgroups
## Configure Hostgroup Parameters
The default values for the host group parameters are specified in the dell-poc.yaml.erb file. This file consists of a couple of sections. The top section contains parameters that are most commonly changed. Under normal situations, the parameters in the remaining sections should not be changed.
Below are listed the parameters that should be changed for each environment. The remaining parameters are noted within the file.
passwd_auto	The password to use in most places.
controller_admin_host	The IP address of the controller nodes interface that has administrative network traffic.
controller_priv_host	The IP address of the controller nodes interface connected to the Private API network.
controller_pub_host	The IP address of the controller nodes interface connected to the Public API network.
nova_public_net	Network address and mask for the Nova Public Network
nova_public_iface	Compute nodes interface that is connected to the Nova Public Network
nova_private_net	Network address and mask for the Nova Private Network
nova_private_iface	Compute nodes interface that is connected to the Nova Private Network
private_api_net	Network address and mask for the Private API Network
private_api_iface	Compute nodes interface that is connected to the Private API Network

Table 3.1.1:
Caution should be taken when changing parameters since the parameter type is determined when it is defined in the dell-poc.yaml.erb file.
When changing values, ensure the new value is in the same syntax as the previous one. Whether a parameter is enclosed in quotes, square brackets, or spans multiple lines determines the type of parameter.
Edit the dell-poc.yaml.erb file and make the appropriate changes.
## Apply hostgroup parameters
The rubygen-foreman_api package must be installed to apply the changes in the dell-poc.yaml.erb file.
# yum install -y rubygem-foreman_api

Change to the /usr/share/openstack-foreman-installer directory and execute the bin/quickstack_defaults.rb command as shown below.
# cd /usr/share/openstack-foreman-installer
# bin/quickstack_defaults.rb -g config/hostgroups.yaml -d ~/dell-poc.yaml.erb -v parameters

The network_overrides parameter cannot easily be set using the dell-poc.yaml.erb file. It is set using the hammer sc-param update command.
First, the parameter ID must be determined, then the settings applied. Replace VLAN with the starting VLAN number to be used in the environment. Make sure the syntax of the line does not change.
# ParamId=$( hammer sc-param list --per-page 1000 --search network_overrides \
 | awk '/network_overrides/ {print $1}')
# hammer sc-param update --id ${ParamId} \
 --default-value "{'vlan_start': VLAN, 'force_dhcp_release': 'false'}" --override yes

# Configure Nodes
After the nodes are installed, the must have a host group assigned to them.
The IDs of the host groups must be determined. Execute the hammer hostgroup list command. Take note of the IDs for the Controller (Nova Network) and Compute (Nova Network) host groups.
# hammer hostgroup list
## Add Controller hostgroup
Apply the Controller (Nova Network) host group to the controller node using the hammer host update command.
# hammer host update --hostgroup-id HOSTGROUP_ID --id HOST_ID

Once the host group is applied, log into the controller node and execute the following command to pull the host group configuration.
# puppet agent -t -dv |& tee /root/puppet.out

This command pipes a copy of the output to the /root/puppet.out file for later review. Watch the output or review the /root/puppet.out file for errors.
## Add Compute hostgroup
Add the host groups to the hosts one at a time. Make sure to run puppet agent -t -dv |& tee /root/puppet.out between each.
Do not add the next host in the list until the previous one is finished. Failure to do so can lead to a race condition that prevents proper installation and configuration of the compute nodes.
# hammer host update --hostgroup-id HOSTGROUP_ID --id HOST_ID
Wait for each compute node to finish its configuration before starting the next one.